## Slide 1
Zivid One+
3D cameras

## Slide 2
Our mission is human-like
vision for robots
Notes: Robot- and industrial automation require human-like vision to operate in “our world”.

## Slide 3
Our mission is human-like
vision for robots
Notes: 3D
Color
High dynamic range
Accurate

## Slide 4: Zivid 3D vision technology
Time coded structured light 3D cameras
Details and colors
HD resolution
Native 3D RGB
High dynamic range
3D HDR
Accurate
High precision and trueness
30 cm to 3m
Working distance
Fast
> 10 FPS burst
< 100ms acquisition time

## Slide 5
Zivid One+
Developer’s introduction

## Slide 6: Zivid One+
HD + Color
2.3 Megapixels
1920 x 1200 resolution
Native 3D RGB
HDR
Extended dynamic range
Multi-frame 3D HDR merge
Fast
Up to 13 FPS burst
Down to 80 ms acquisition time
Accurate
ZO+ Small: 25 µm point precision
ZO+ Medium: 60 µm point precision
ZO+ Large: 225 µm point precision
Time coded structured light
3D camera
Notes: Accuracy
Zivid One+ M at D = 600mm, La = 200 lux

## Slide 7: Zivid One+
Model | S | M | L
Max distance | 1.0 m | 2.0 m | 3.0 m
Optimal working distance | 0.3 to 0.8 m | 0.6 to 1.6 m | 1.2 to 2.6 m
Key applications | Tiny to small objects Trays and boxes | Small to medium objects Totes and bins | Medium to large objects Standard EU/US pallets
3D camera line-up
Notes: + precision
+ key applications

## Slide 8: Zivid One+ S
Field of view
160 x 130 mm at 0.3 m (min distance)
620 x 440 mm at 1.0 m (max distance)
0.3 to 0.8 m optimal working distance
Full overlap between 0.45 to 0.6 m
Spatial resolution
0.12 mm at 0.3 m
0.32 mm at 0.8 m
0.40 mm at 1.0 m
Tiny to small objects – trays / boxes
Point precision
25 µm at 0.3 m
105 µm at 0.8 m
180 µm at 1.0 m

## Slide 9: Zivid One+ M
Field of view
430 x 270 mm at 0.6 m (min distance)
1330 x 870 mm at 2.0 m (max distance)
0.6 to 1.6 m optimal working distance
Full overlap between 0.7 to 1.3 m
Spatial resolution
0.23 mm at 0.6 m
0.6 mm at 1.6 m
0.75 mm at 2.0 m
Small to medium objects – totes / bins
Point precision
60 µm at 0.6 m
570 µm at 1.6 m
900 µm at 2 m

## Slide 10: Zivid One+ L
Medium to large objects – standard EU/US pallets
Field of view
843 x 530 mm at 1.2 m
2069 x 1310 mm at 3.0 m
1.2 to 2.6 m optimal working distance
Full overlap between 0.8 to 2.5 m
Spatial resolution
0.45 mm at 1.2 m
0.96 mm at 2.6 m
1.11 mm at 3.0 m
Point precision
225 µm at 1.2 m
1630 µm at 2.6 m
2500 µm at 3.0 m

## Slide 11: Zivid One+
Aperture |  | f/1.4 to f/32 | 9 stop range
Shutter |  | 1/154 to 1/10 s | 4 stop range
Gain |  | 1x to 16x | 4 stop range
Brightness |  | 1/8x to 1.8x | 4 stops range 400 lumens at 1x 720 lumens at 1.8x
Exposure controls
Notes: Aperture
Shutter speed
Imager gain (version v1.3)
Projection brightness

## Slide 12: Zivid One+ speed
3D burst |  | 
2-frame 3D HDR burst |  | 
3-frame 3D HDR burst |  | 
5-frame 3D HDR burst |  | 
Up to 13 FPS
Up to 6 FPS
Up to 3 FPS
Up to 1 FPS
Notes: Tac = 12 x Tshutter +

## Slide 13
Non laser based Inherently safe for collaborative use
White light source Native color capabilities and broad material coverage Good data on most materials and surfaces Functional diversity and highly repurposable | 
Non laser based | 
Eye safe and less annoying No dangerous direct reflections from e.g. shiny objects No need for Laser Safety Officer or similar | 

## Slide 14: Understanding Zivid 3D camera accuracy
ISO 5725
Precision Describing random errors, a measure of statistical variability.
Trueness Describing systematic errors, a measure of statistical bias.
Accuracy Describing a the combination of random and systematic errors. Sum of Precision and Trueness.

## Slide 15: ISO 5725 and 3D cameras
TARGET SCENE
Precision random errors
Precision, trueness and accuracy applied
Lower accuracy
Higher accuracy
Trueness deviation from true reference

## Slide 16: Datasheet specifications
Specifications
Point precision
Local planarity precision
Global planarity trueness and accuracy
Dimension precision, trueness and accuracy
Conditions
Working distance
Ambient temperature
Ambient light
Aperture
Imager Gain
Projector brightness

## Slide 17: Point metrics
Zivid One+ M - typical specifications
Conditions, unless otherwise specified: Ambient temperature (Ta) = 25C Ambient light (La) = 200 lux Aperture (A) = f/5.6
Projector brightness (Pb) = 1x Imager gain (Ig) = 1x
Point precision | 60 | um
La = 750 lux | 70 | um
D = 1600mm | 570 | um
D = 1600mm, Pb = 1.8x | 480 | um
Notes: Incuding spatial resolution
One per model?

## Slide 18: Point metrics
Zivid One+ M - typical specifications
Conditions, unless otherwise specified: Ambient temperature (Ta) = 25C Ambient light (La) = 200 lux Aperture (A) = f/5.6
Projector brightness (Pb) = 1x Imager gain (Ig) = 1x
Point precision vs. working distance
Notes: Incuding spatial resolution
One per model?

## Slide 19: Global planarity metrics
Zivid One+ M - typical specifications
Global
Conditions, unless otherwise specified: Ambient temperature (Ta) = 25C Ambient light (La) = 200 lux Aperture (A) = f/5.6
Projector brightness (Pb) = 1x Imager gain (Ig) = 1x
Global planarity trueness | 90 | um
D = 1600mm | 670 | um
D = 1600mm, Pb = 1.8x | 690 | um
Global planarity accuracy | 140 | um
D = 1600mm | 1030 | um
D = 1600mm, Pb = 1.8x | 1000 | um
Notes: Incuding spatial resolution
One per model?

## Slide 20: Zivid One+ M
Point metrics – typical specifications
Conditions, unless otherwise specified: Ambient temperature (Ta) = 25C Ambient light (La) = 200 lux Aperture (A) = f/5.6 Distance (D) = 600mm
Projector brightness (Pb) = 1x Imager gain (Ig) = 1x
Point precision | 60 | um
La = 750 lux | 70 | um
D = 1600mm | 570 | um
D = 1600mm, Pb = 1.8x | 480 | um
D = 1500mm, La = 500 lux, Pb = 1.8x | 570 | um
Notes: Incuding spatial resolution
One per model?

## Slide 21: Zivid One+ M
Local planarity metrics – typical specifications
Conditions, unless otherwise specified: Ambient temperature (Ta) = 25C Ambient light (La) = 200 lux Aperture (A) = f/5.6 Distance (D) = 600mm
Projector brightness (Pb) = 1x Imager gain (Ig) = 1x
Local planarity precision | 90 | um
La = 750 lux | 100 | um
D = 1600mm | 610 | um
D = 1600mm, Pb = 1.8x | 540 | um
D = 1500mm, La = 500 lux, Pb = 1.8x | 630 | um
Local
Notes: Incuding spatial resolution
One per model?

## Slide 22: Zivid One+ M
Global planarity metrics – typical specifications
Conditions, unless otherwise specified: Ambient temperature (Ta) = 25C Ambient light (La) = 200 lux Aperture (A) = f/5.6 Distance (D) = 600mm
Projector brightness (Pb) = 1x Imager gain (Ig) = 1x
Global planarity trueness | 90 | um
D = 1600mm | 670 | um
D = 1600mm, Pb = 1.8x | 690 | um
Global planarity accuracy | 140 | um
D = 1600mm | 1030 | um
D = 1600mm, Pb = 1.8x | 1000 | um
Global
Notes: Incuding spatial resolution
One per model?

## Slide 23: Zivid One+ M
Dimension metrics – typical specifications
Conditions, unless otherwise specified: Ambient temperature (Ta) = 25C Ambient light (La) = 200 lux Aperture (A) = f/5.6 Distance (D) = 600mm
Projector brightness (Pb) = 1x Imager gain (Ig) = 1x
Dimension precision | 170 | um
D = 1600mm | 380 | um
Dimension trueness | < 1.0 | %
Dimension accuracy | < 1.0 | %
Notes: Measuing 5x 20mm squares

## Slide 24: Zivid One+
Industry ready design
Rugged design | Aluminum body IP65 water and dust 5G Random (10-55Hz) 15G Shock
Size and weight | 226x86x165mm 1980g
Data and power | USB 3.0 SuperSpeed type-B 24V 5A DC
Certifications | CE FCC Class A
Operating conditions | 10 to 40C
Notes: 3x reference scenes with settings

## Slide 25: The Zivid One+ solution
Zivid One+ | Zivid Studio | Zivid SDK
Award winning 3D color cameras [S/M/L] High performance & industrial grade. | Explore, evaluate and learn. A highly modern UI for point cloud capturing with Zivid 3D color cameras | The essential tool suite for machine vision software development, cross-platform and GPU accelerated.
Notes: Zivid provides
Zivid One 3D color camera
Zivid API - drivers that produce a hi-res point cloud with color info
Zivid Studio – GUI to view, measure and optimize settings

## Slide 26: Zivid Studio
Capture high-quality 3D point clouds Single or multi-frame HDR. Manual or automatic with Capture Assistant
View captured 3D data Explore 3D data, 2D depth map or corresponding 2D color image.
Controls and filters Configure settings and filters per frame, and combine frames for 3D HDR. Use Histogram feature to get the best exposures per capture.
The easy to use application for
Point cloud capture and exploration
Explore sample scenes at
zivid.com/images

## Slide 27: Zivid SDK
Core
ZVE 2
Zivid Vision Engine
Hardware drivers
Camera Control
Libraries
Example Applications
Tools & Utilities
Simplified block diagram
The essential tool suite for developing machine vision software with Zivid 3D cameras
Core API
Cross platform
x86-64
Linux and Windows
Language & wrappers
Native: C++ / .NET
Wrappers: Genicam
Zivid Vision Engine
GPU accelerated point cloud computations

## Slide 28: Getting Started
Quick Start Guide | zivid.com/start
Zivid One+ datasheet | zivid.com/downloads
Point cloud examples | zivid.com/images
Free 1:1 online demo | zivid.com/schedule-a-free-zivid-demo
Developer kits | zivid.com/order

## Slide 29: Learn more at www.zivid.com Human-like vision for robots